Patch cord management 0.5HU for 19” modular HD patch panels

to be used with 0.5HU, 1.0HU and 3.0HU modular patch panels of the HD3-ES and HD3 series.

For secure patch cord management and routing on the front side of the panel.

With bend-radius support on both ends.

With plastic retainers 38 x 28 mm on both ends, opening on the top.

Two hinged plates with a total of 4 label holders.

4 Labels 95 x 8 mm included.

Mounts to the panels using the 19” rack mount screws.

Features:

Material:            2 mm sheet steel, painted

Colour:              black like RAL 9005

Depth (mounted):     65mm

Height:              0.5HU

Manufacturer:        Telegärtner

Type:                HD3-ES patch cord management

Part No.:            H02025A4001