# FO HD patch module 1.0 HU, 18 x LCD, OM3

for the connection of breakout, mini-breakout and pre-terminated fiber optic cables;

to be used in HD3 modular patch panels,

self-locking mechanism with spring steel latches;

front panel with 18 LC duplex adapters, arranged in three rows of 6 adapters;

dust protection plugged in on both sides of the adapters.

Cable fixation for 6 cables.

Features:

Width:       102.5 mm

Height:      35.0 mm

Depth:       90.0 mm

Material:    0.7 mm sheet steel

Surface:     conductive for improved bonding

Colour:      black

LCD adapter:

- Standard:  IEC 61754-20

- Sleeve:    ceramic

- Housing:   pastic

- Colour:    aqua

- Designed for OM3 and OM4 applications

- Dust protection

Manufacturer:   Telegärtner

Type:           HD3 patch module 1.0 HU

Part No.:       H02050A4005