# FO HD fanout module type A 1.0 HU, 18 x LCD, OM4

with MPO/MTP(R) adapter on the reverse side;

to be used in HD3 modular patch panels,

self-locking mechanism with spring steel latches;

front panel with 18 LC duplex adapters with dust protection plugged in;

module housing with angled rear with 3 MPO/MTP(R) adaptors type A.

3 fanout kit installed inside of the module.

Housing cover with laser warning and four opening aids.

Features:

Width:       102.5 mm

Height:      35.0 mm

Depth:       122.0 mm

Material:    0.7 mm sheet steel, painted

Colour:      black

Fanout kit:

- Fiber type: acc. to IEC60793-2-10

- Secondary coating: max. 900 µm, coloured

- Crush resistance: min. 1000 N/m

- Inserion loss: max. 1.0 dB/km @ 1300 nm

- Modal bandwidth: min. 3500 MHz x km @ 850nm

- Plug 1: LC acc. to IEC61754-20

- Mating cycles: min. 1000

- Ferrule: Ceramic

- RL: min. 30 dB

- Plug 2: MPO/MTP(R) male acc. to IEC61754-7

- Mating cycles: min. 1000

- Ferrule: Composite

- RL: min. 30 dB

LCD adapter:

- Standard:  IEC 61754-20

- Sleeve:    ceramic

- Housing:   pastic

- Colour:    violet

- Designed for OM4 applications

- Dust protection

Manufacturer:      Telegärtner

Type:              HD3 FanOut module 1.0 HU

Part No.:          H02050A4016