# FO HD splice module 0.5 HU, 6 x LCD, OM5

for the connection of loose tube cables,

to be used in HD3 modular patch panels,

self-locking mechanism with spring steel latches;

front panel with 6 LC duplex adapters with dust protection plugged in;

with splice cassette with integrated splice holders for 12 crimp and micro heat shrink splice protectors.

with pigtails installed;

pigtails stripped ready to be spliced and routed in splice cassette.

Pigtails in 12 different colours according to IEC 60304.

Plugs of pigtails plugged in the adaptors.

Housing cover with four opening aids.

Module has two cable entries on the rear, one of which is closed and can be opened on site.

Features:

Width:       102.5 mm

Height:      17.5 mm

Depth:       147.0 mm

Material:    0.7 mm sheet steel, painted

Colour:      black

Pigtail:

- Fiber type: acc. to IEC60793-2-10

- Secondary coating: max. 900 µm, coloured

- Crush resistance: min. 1000 N/m

- Inserion loss: max. 1.0 dB/km @ 1300 nm

- Modal bandwidth: min. 3500 MHz x km @ 850nm

- Plug: LC acc. to IEC61754-20

- Mating cycles: min. 1000

- Ferrule: Ceramic

- RL: min. 30 dB

LCD adapter:

- Standard:  IEC 61754-20

- Sleeve:    ceramic

- Housing:   pastic

- Colour:    lime green

- Designed for OM5 applications

- Dust protection

Manufacturer:      Telegärtner

Type:              HD3 splice module 0.5 HU

Part No.:          H02050A4025