FO HD patch module 1.0HU, 12xLC/APCD, OS2, laser protection

for the connection of breakout, mini-breakout and pre-terminated fiber optic cables;

to be used in HD3-ES modular patch panels,

tool-free mounting with knurled screw;

front panel with 12 LC/APC duplex adapters with integrated laser protection, dust protection plugged in;

cable fixation for 12 cables (2 cables per peg).

Features:

Width:       118.0 mm

Height:      36.0 mm

Depth:       104.5 mm

Material:    1.5 mm sheet steel, painted

Colour:      black

LCD adapter:

- Standard:  IEC 61754-20

- Sleeve:    ceramic

- Housing:   pastic

- Colour:    green

- Designed for OS1 and OS2 applications

- Integrated laser protection

- Dust protection

Manufacturer:      Telegärtner

Type:              HD3-ES patch module 1.0HU

Part No.:          H02050A4076