FO HD patch module 0.5HU, 6xMPO-A

for the connection of pre-terminated fiber optic cables.

to be used in HD3-ES modular patch panels,

tool-free mounting with knurled screw;

front panel with 6 MPO/MTP(R) adapters type A (key up to key down);

dust protection plugged in on both sides of the adapters.

Cable fixation for 6 cables.

Features:

Width:       118.0 mm

Height:      17.0 mm

Depth:       104.5 mm

Material:    1.5 mm sheet steel, painted

Colour:      black

MPO/MTP(R) adapter:

- Standard:  IEC 61754-7-1 and -7-2

- Housing:   pastic

- Colour:    black

- Designed for OM3, OM4, OM5, OS1 and OS2 applications;

- Dust protection

Manufacturer:      Telegärtner

Type:              HD3-ES patch module 0.5HU

Part No.:          H02050A4080