FO HD splice module 0.5HU, 6xLCD, OM5, laser protection

for the connection of loose tube cables.

to be used in HD3-ES modular patch panels,

tool-free mounting with knurled screw;

front panel with 6 LC duplex adapters with integrated laser protection, dust protection plugged in;

with splice cassette with integrated splice holders for 12 crimp and micro heat shrink splice protectors.

with pigtails installed;

pigtails stripped ready to be spliced and routed in splice cassette.

Pigtails in 12 different colours according to IEC 60304.

Plugs of pigtails plugged in the adaptors.

Housing cover with opening aids.

Module has 2 cable entries on the rear.

Features:

Width:       118.0 mm

Height:      17.0 mm

Depth:       147.0 mm

Material:    1.0 mm sheet steel, painted

Colour:      black

Pigtail:

- Fiber type: acc. to IEC60793-2-10

- Secondary coating: max. 900 µm, coloured

- Crush resistance: min. 1000 N/m

- Inserion loss: max. 1.0 dB/km @ 1300 nm

- Bandwidth: min. 3500 MHz x km @ 850 nm

- Plug: LC acc. to IEC61754-20

- Mating cycles: min. 1000

- Ferrule: Ceramic

- RL: min. 30 dB

LCD adapter:

- Standard:  IEC 61754-20

- Sleeve:    ceramic

- Housing:   pastic

- Colour:    lime green

- Designed for OM5 applications

- Integrated laser protection

- Dust protection

Manufacturer:      Telegärtner

Type:              HD3-ES splice module 0.5HU

Part No.:          H02050A4085