FO HD fanout module 1.0HU, 12xLCD, OM4, laser protection, type A

with MPO/MTP(R) adapter type A on the reverse side;

to be used in HD3-ES modular patch panels,

tool-free mounting with knurled screw;

front panel with 12 LC duplex adapters with integrated laser protection, dust protection plugged in;

module housing with angled rear with 2 MPO/MTP(R) adaptors type A (key-up to key-down).

Fanout kit installed inside of the module.

Housing cover with laser warning, fiber-port-assignment and opening aids.

Features:

Width:       118.0 mm

Height:      36.0 mm

Depth:       123.5 mm

Material:    1.0 mm sheet steel, painted

Colour:      black

Fanout kit:

- Fiber type: IEC 60793-2-10, OM4

- Secondary coating: max. 900 µm, coloured

- Crush resistance: min. 1000 N/m

- Inserion loss: max. 1.0 dB/km @ 1300 nm

- Plug 1: LC acc. to IEC61754-20

- Mating cycles: min. 1000

- Ferrule: Ceramic

- RL: min. 30 dB

- Plug 2: MPO/MTP(R) male acc. to IEC61754-7-1

- Mating cycles: min. 1000

- Ferrule: Composite

- RL: min. 30 dB

LCD adapter:

- Standard:  IEC 61754-20

- Sleeve:    ceramic

- Housing:   pastic

- Colour:    violet

- Designed for OM4 applications

- Integrated laser protection

- Dust protection

Manufacturer:      Telegärtner

Type:              HD3-ES FanOut module 1.0HU

Part No.:          H02050A4094