FO duplex patch cord LC/APC-HD-D Uniboot, OS2, 2.5m

with high density LC/APC duplex Uniboot connectors on both ends;

plugs have push-/pull latch for improved grip;

fiber polarity can be changed without using tools;

individual plugs have red or black ring for clear fiber identification and cable polarity (A-B/A-A).

Pre-assembled dust covers.

Colour of connectors and cable jacket as specified by ANSI/TIA.

Features:

Length:                 2.5m

Tensile strength:       100N

RoHS:                   compliant

Connector

- Type:                 IEC61754-20 LC/APC

- Performance class:    grade B

- Ferrule:              zirconia ceramic

- Housing:              plastic

- Colour:               green

- Insertion loss (IL):  typ. ≤ 0.06dB

- Return loss (RL):     ≥ 85dB

- Mating cycles:        ≥ 1000

Cable:

- Type:                 I-K(ZN)H

- Outer diameter:       ≤ 2.0mm

- Colour:               yellow

Fiber:

- Type:                 E9/125 G.657.A1 OS2

- Insertion loss (IL):  ≤ 0.4dB/km @ 1310nm

Manufacturer:      Telegärtner

Type:              FO patch cord LC-HD-D Uniboot

Part number:       L00872U0002